## Slide 1: Self-Organizing Networks in LTE:
a Q-learning Approach to ABS Optimization

## Slide 2: Self-Organizing Networks (SON)
In 2016, global mobile data traffic amounted to 7 exabytes (EB) per month;
in 2021, mobile data traffic worldwide is expected to reach 49 EB per month at a compound annual growth rate of 47%;
To keep the pace of this incoming scenario, an efficient solution is needed: exploit heterogeneous networks (HetNet) and make the systems more autonomous and automated;
The concept of Self-Organizing Networks (SON) is a possible approach to achive these goals.

## Slide 3
The SON functions are usually categorized into three main groups:
  Self-Planning: identify the parameter settings of new network elements;
  Self-Deployment: make a “plug and play” approach for each new node;
  Self-Healing: execute routine actions that keep the network operational and prevent problems;
  Self-Optimization: collect performance indicators from User Equipments (UEs) and the base stations (eNodeB) to auto-tune the network settings.
The paper is focused on the last point of the list, precisely on the improvement of the signal quality and so of the throughput in a LTE system;
We aim to minimize the interference in a HetNet, made of micro and macro cells, with an adaptive coordination in downlink transmissions of the antennas, controlling the transmit power patterns.

## Slide 4: Enhanced Inter Cell Interference Coordination (eICIC)
Micro cells are low power nodes, however they