## Slide 1: Self-Organizing Networks in LTE:
a Q-learning Approach to ABS Optimization

## Slide 2: Self-Organizing Networks (SON)
In 2016, global mobile data traffic amounted to 7 exabytes (EB) per
month;
in 2021, mobile data traffic worldwide is expected to reach 49 EB per month at a compound annual growth rate of 47%;
To keep the pace of this incoming scenario, an efficient solution is needed: exploit heterogeneous networks (HetNet) and make the systems more autonomous and automated;
The concept of Self-Organizing Networks (SON) is a possible approach to achive these goals.

## Slide 3
The SON functions are usually categorized into three main groups:
  Self-Planning: identify the parameter settings of new network elements;
  Self-Deployment: make a “plug and play” approach for each new node;
  Self-Healing: execute routine actions that keep the network operational and prevent problems;
  Self-Optimization: collect performance indicators from User Equipments (UEs) and the base stations (eNodeB) to auto-tune the network settings.
Our work is focused on the last point of the list, precisely on the improvement of the signal quality and so of the throughput, in a LTE system;
We aim to minimize the interference in a HetNet, made of micro and macro cells, with an adaptive coordination in downlink transmissions of the antennas, controlling the transmit power patterns.

## Slide 4: Enhanced Inter Cell Interference Coordination (eICIC)
Micro cells (radius 10-300m) are low power nodes and provide high capacity to UEs. Macro cells (radius up to 20km) are high power nodes with a smaller capacity.
Since they share the same frequencies, the latter severly degredes the downlink transmission of the former and an UE might connect to a macro instead of a micro, because it senses a stronger received power from high-power node.
The solution, implemented in LTE 3GPP standard, is known as enhanced Inter Cell Interference Coordination (eICIC) and macro gets silent for an amount of time called Almost Blank Subframe (ABS).
So the challenge is to find the optimal number and pattern of ABS in a frame to improve the involved system.